## Slide 1: NON INVASIVE POSITIVE PRESSURE VENTILATION
DR.REZA ALIZADEH KASHANI, MD , FCCM

## Slide 2: Types of mechanical ventilation
Invasive mechanical ventilation (IMV)
Non-invasive mechanical ventilation (NIV)
High low nasal cannula ventilation (NIV-HFNC)

## Slide 3: NON INVASIVE MECHANICAL VENTILATION

## Slide 4: HISTORY
From 1990 to the present, the use of NIV by IPPV progressively increased in acute care.
This technique is used in up to 30–40 percent of patients in critical care units.

## Slide 9: RESMED

## Slide 10: PHILIPS

## Slide 13: NIV MODES

## Slide 14: SPONTANEUS NEGATIVE PRESSURE VENTILATION

## Slide 16: PRESSURE = FLOW × RESISTANCE + VOLUME / COMPLIANCE

## Slide 17: IPAP – EPAP = PRESSURE SUPPORT

## Slide 18
EPAP = 5 CMH2O
PSV = 10 CMH2O
IPAP = 15 CMH2O
EPAP = PEEP
PSV = PRESSURE SUPPORT
IPAP = PIP
EPAP = 10 CMH2O
IPAP = 25 CMH2O
PSV = 15 CMH2O

## Slide 20: Continuous positive airway pressure
no additional pressure is applied during inhalation.
With NIV, pressure applied to the airway during the inspiratory phase is greater than the pressure applied during exhalation
provides respiratory muscle assistance,
increased tidal volume
the most common use of CPAP mode is for the treatment of obstructive sleep apnea.

## Slide 23: CPAP SETTING
CPAP = 5 CMH2O
FIO2 = 50 %

## Slide 24: Pressure support ventilation (S MODE)
Pressure support ventilation is used most commonly for NIV
IPAP and EPAP are set,
but there is no backup rate.

## Slide 26: S MODE SETTING
EPAP = 5 CMH2O
PSV = 10 CMH2O OR IPAP = 15 CMH2O
FIO2 = 50 %

## Slide 27: spontaneous/timed (S/T) mode
if the patient becomes apnoeic, the ventilator will deliver breaths at the rate set on the ventilator.

## Slide 29: S/T MODE SETTING
EPAP = 5
IPAP = 15
RR = 12
FIO2 = 50
TRIGGER = 2
I – TIME = 1 S

## Slide 30: Pressure-controlled ventilation
Pressure-controlled ventilation is similar to pressure support in that the ventilator applies a fixed level of pressure with each breath.
Two differences:
there is a backup rate with pressure control ( RR )
the inspiratory time is fixed ( I-TIME )
the fixed inspiratory time of pressure control is beneficial when the inspiratory phase is prolonged during pressure support due to leak

## Slide 31: average volume assured pressure support (AVAPS)
AVAPS maintains a tidal volume equal to or greater than the target tidal volume , by controlling the pressure support between the minimum and maximum IPAP settings.
If patient effort decreases, AVAPS automatically increases IPAP to maintain the target tidal volume.
If patient effort increases, AVAPS will reduce IPAP

## Slide 34: AVAPS MODE SETTING
EPAP = 5
MAX IPAP = 30
MIN IPAP = 15
TV = 500
RR = 12
FIO2 = 50
I-TIME = 1
TRIGGER = 2

## Slide 36: APRV (Airway Pressure Release Ventilation )

## Slide 38: APRV SETTING
P high is usually set at a level between 20 and 30 cm H2O.
P low is set between 0 and 5 cm H2O initially.
T high: 4–6 s
T low: 0.2-0.8 seconds

## Slide 39: Proportional assist ventilation
the applied pressure is determined by respiratory drive (inspiratory flow and tidal volume) and lung mechanics ( resistance and compliance),
the proportion of assist is set by the user.
improve patient tolerance during acute respiratory failure.

## Slide 40
The support given is a proportion of the patient's effort and is normally set at 70 - 80%.
This support is always changing according to patient's effort and lung dynamics.
If the patient's effort and/or demand are increased, the ventilator support is increased

## Slide 42: Neurally adjusted ventilatory assistance (NAVA)
ventilator is triggered by electrical activity of a diaphragm
good synchrony

## Slide 43: Volume-controlled ventilation
fixed tidal volume and inspiratory flow
More complicated to use
Wide range of alarms
Breath-stacking possible

## Slide 44: Rise time
Rise time is the time required to reach inspiratory pressure at the onset of the inspiratory phase with pressure support .

## Slide 45: How to start a patient on non-invasive ventilation

## Slide 46: Education
Plan an adequate training of all staff

## Slide 47: Environment
Choose the setting where to start NIV according to the severity of ARF

## Slide 48: Indication
Select patients

## Slide 49: Recommendations for PATIENT SELECTION
Strong positive evidence
Exacerbation of COPD
Acute cardiogenic pulmonary edema
Acute respiratory failure in immunocompromised patients
Prevention of weaning failure in high-risk patients
Likely positive effect
Post-operative respiratory failure
Chest trauma
Support during endoscopy

## Slide 50: Long-term conditions that cause CRF leading to NIV
Muscular-skeletal : Scoliosis , kyphoscoliosis
Neuro-muscular : Duchenne , Amylotrophic lateral sclerosis , Myasthenia gravis
Neurological : central hypoventilation
Obesity : obstructive sleep apnea
Pulmonary : COPD , Cystic fibrosis, pulmonary hypertension

## Slide 51: negative evidence
Cardiac or respiratory arrest
agitation not controlled with sedation
Severe gastrointestinal bleeding
Bowel obstruction
Severe hemodynamic instability
Fixed upper airway obstruction
Inability to clear secretions
Untreated pneumothorax

## Slide 52: Strong negative evidence
extubation failure

## Slide 53: When to Start NIV in acute patients?
Clinical signs
Rest dyspnea (from moderate to severe)
Tachypnea (RR >25 breaths/min)
Increased respiratory work (accessory muscles use, paradoxical breathing)
Respiratory acidosis (pH <7.35 with PaCO2 > 45 mmHg)
Hypoxemia (PaO2 /FiO2 <300)

## Slide 54: Information
Explain the technique to patients

## Slide 55: Equipment
Choose the mask best fitting facial anatomy
Choose a ventilator

## Slide 56: Starting ventilation
Start with low pressures, then increase gradually depending on comfort.

## Slide 57: Monitoring
Check clinical status, monitor SpO2
measure blood gases periodically
patient–ventilatory synchrony, comfort, leaks
Consider humidification
carefully sedation
management of secretions
Prevent skin lesions

## Slide 58: Predictors of NIV failure Before starting ventilation
RR > 35 breaths/min
Moderate–severe ARDS (P/F R <200)
Shock (systolic blood pressure <90 mmHg )
Multiple acute organ insufficiency
acidosis (pH <7.25)
Severe altered level of consciousness
Excessive secretions
Low BMI
Age >40 year

## Slide 59: Predictors of NIV failure After starting ventilation
Failure to improve oxygenation within first hour of NIV
(PaO2/FiO2 <175 mm Hg)
No improvement within 2 h of NIV in pH, RR , PaCO2
Inability to minimise leak
Inability to co-ordinate with NIV
Burden of secretion

## Slide 60: HIGH FLOW NASAL CANNULA

## Slide 61
higher flow of oxygen,
warm and humidified oxygen
causes the patient to rebreathe less exhaled air (the elimination of CO2)
small amount of PEEP

## Slide 62
High-flow nasal cannulas will aerosolize the COVID-19 virus