## Slide 1: Serological Tests and their Quality Controls in Medical Lab
Farimah Masoumi, PhD
Tehran University of Medical Sciences

## Slide 2: Immunology Forever!

## Slide 3: Outlines
Principles of Serology
Agglutination
Precipitation
Immunoassays
Serological Tests in Medical labs
Safety in Serology Lab
Quality Control

## Slide 4
Affinity
Avidity
Ag:Ab Ratio
Ag physical form
Outcome of
Ag-Ab reaction
Antibody: Antigen Reaction
beginning for serological tests

## Slide 5: Serology: diagnostic identification of antibodies in the serum

## Slide 7
Soluble
Soluble
Precipitation
Soluble
Insoluble
Agglutination
Soluble
Soluble
Passive Agglutination
Soluble
Soluble
Reverse Passive Agglutination
Notes:   Red blood cells
  Polystyrene latex
  Charcoal

## Slide 8: Ag-Ab ratio

## Slide 9: Physical form of Ag
Soluble
Particulate
Antigenic form
Precipitation
Agglutination

## Slide 10
the process whereby specific antigens (e.g., red blood cells) aggregate to form larger visible clumps when the corresponding specific antibody is present in the serum.
Agglutination

## Slide 11: RBC surface antigens are another example of particulate Antigens
The process is called “Hemagglutination”
Antibodies are called “Hemagglutinins”

## Slide 13: Sometimes an anti-antibody is needed to see the agglutination!
The serum containing anti-human antibody is called “Coombs serum”

## Slide 14: Bacterial antigens are an example of particulate antigens

## Slide 15: Bacterial agglutination

## Slide 16: Physical form of Ag
Soluble
Particle
Antigenic form
Precipitation
Agglutination
Liquid
Semiliquid
Liquid only

## Slide 17
combination of soluble antigen with soluble antibody to produce a visible insoluble complex.
Precipitation

## Slide 18: Precipitation in liquid

## Slide 20: Measurement of Precipitation by Light Scattering
Turbidometry
Nephlometry

## Slide 21: Precipitation in gel!

## Slide 22: Double immunodiffusion
Ag
Ab
Zone of equivalence

## Slide 23: Double immunodiffusion

## Slide 24: Single Radial Immunodiffusion (SRID)
Ab (or Ag) mixed with the gel
Ag

## Slide 25: Radial immunodiffusion

## Slide 26: Quantifying SRID

## Slide 27: Counterimmunoelectrophoresis (CEP)
Ag
Ab
-
-
-
-
+
+
+
+

## Slide 28: Immunoelectrophoresis
Ag
-
-
-
-
+
+
+
+
Ab

## Slide 29: Immunoelectrophoresis

## Slide 30
Determine concentration of a macromolecule in a solution through the use of an antibody
Immunoassay

## Slide 32
Macromolecule (Ag)

## Slide 33
Label

## Slide 34
Label
Enzyme
Radioactive
Fluorescence
Chemiluminesence

## Slide 35
Label
Enzyme
Radioactive
Fluorescence
Chemiluminescent
Enzyme Immunoassay (EIA)
Radio Immunoassay (RIA)
Fluorescence Immunoassay
(FIA)
Chemiluminescence Immunoassay
(CIA )

## Slide 36: Other forms of signals!
Labeled Antibodies
Color (ELISA)
Radioactivity (RIA)
Fluorescence (IF)
Luminescence

## Slide 37: Homogenous vs. Heterogeneous Immunoassays

## Slide 38: ELISA generates color

## Slide 39: Direct ELISA
E
E
E
S
Color

## Slide 40: Direct ELISA to detect an Ag
E
E
E
S
Color

## Slide 41: Indirect ELISA
E
E
S
Color
E

## Slide 42: Indirect ELISA to detect an Ag
E
E
S
Color
E

## Slide 43: Indirect ELISA to detect an Ab
S
Color
E

## Slide 44: Sandwich ELISA
S
Color
E
E

## Slide 45: Autoanalyzers designed based on different forms of signals!
Color (ELISA)
Radioactivity (RIA)
Labeled Antibodies
Fluorescence (ELFA)
Luminescence (ECL)
AIA
VIDAS
COBAS

## Slide 46: What is fluorescence?
absorb high energy photon
emit lower energy photon
ground state

## Slide 47: TOSOH Biosciene : AIA-600 II , AIA-2000

## Slide 48
S
Color
E
E
ALP
ALP
4-MUP
4-MU
EX: 372nm
EM: 445nm
Fluorometric enzyme immunoassay (FEIA)
Notes: 4 methylumberiferil phosphate

## Slide 49: biomerieux: VIDAS/MiniVIDAS

## Slide 51: Advantages
High MTBF: no activity breakdown
No warm-up period
Limited maintenance : saved technician time for added-value tasks
Easy to use: limited training time
Limited quality control and calibration frequency
No water needed
Emergency tests are available

## Slide 52: Roche: Cobas e411

## Slide 53
S
Light
B
B
ECLIA
RU
RU
Strp
Strp

## Slide 54: Technology Elecsys® ECL

## Slide 55: Test Principles
Competitive , analytes of low molecular weight
FT3, FT4, Cortisol, Testosterone, Estradiol
Sandwich, high molecular weight analytes such as,
TSH, FSH, LH
Bridging, similar to the sandwich principle, except that the assay is designed to detect antibodies, not antigens
IgG, IgM, IgA

## Slide 56: Advantages:
• High sensitivity for patient-friendly low sample volumes and fast results due to short turnaround times
Broad measuring range for fewer repeats and a streamlined workflow
High precision over the entire measuring range for reliable results
Can be used to detect all analytes for a broad assay menu including innovative markers

## Slide 57: Serological Tests in Medical labs
Infectious diseases related tests
Non infectious serological tests

## Slide 58: Infectious diagnostic serological tests

## Slide 59: Characteristics of Infectious Diseases Depends on:
The immune status of an individual (Immunocompromised individuals have a much higher rate of microbial disease.)
Overall incidence of an organism in the population
Pathogenicity or virulence of the agent
Presence of a sufficiently large dose of the agent or organism to produce an infection
Appropriate portal of entry

## Slide 60: Immune Response against pathogens
Virus
Bacteria
Fungi
Parasites

## Slide 63: Lab Diagnostics for Bacterial Diseases
Bacterial Culture
Microscopic Visualization
Antigen Detection
Molecular Detection
Serological Diagnosis
Agglutination, ELISA
Advantages
Disadvantages
Notes: S pyogenes (strep throat), L pneumophila (Legionnaire’s disease),
rotavirus (pediatric diarrheal disease), respiratory syncytial virus,
and influenza A and B. Antigen detection assays are highly
specific, and because of advances in technology, sensitivities of
the assays have improved dramatically. In many cases, antigen
detection assays, particularly LFA, have replaced other methods
used to detect infections with bacteria, viruses, and fungi.
For some infectious agents, such as
N gonorrhoeae and C trachomatis, nucleic-acid–based assays are
widely available and clearly the choice for detection.

## Slide 64: Infectious Serological tests
ASO
Wright, 2ME Wright, Coombs Wright
RPR
Widal

## Slide 65: Group A Streptococci (Streptococcus Pyogenes)
Pharengitis & Tonsilitis
    Acute glomerulonephritis
    Acute Rheumatic fever
Pyoderma & Impedigo
  Acute glomerulonephritis

## Slide 66: Common diagnostic methods
Culture by patient specimen
ASO titration
Anti-DNase B
lateral flow assay (LFA )
Notes: However, serological diagnosis must be used to identify acute rheumatic fever and poststreptococcal glomerulonephritis because the organism is unlikely to be present in the pharynx or on the skin at the time symptoms appear.

## Slide 67: Streptococcal Exo-antigens
    Streptolysin O
    DNase
    Hyaluronidase
    Streptokinase
ASO
Anti-Dnase B

## Slide 68: ASO
Classic Way: Neutralization
Normal Rang: 240 Todd units in an adult , 320 Todd units in a child
Nephlometry
Automated, Rapid, Quantitative method
Agglutination

## Slide 69: ASO : Current Commercial Kits!

## Slide 70: Quality Control
Positive and Negative Control
Using clean, fresh sera without hemolysis
Stick to the manufacturers procedure

## Slide 71: Brucellosis (Malta Fever)
Fever & Chills
Sweats
Weakness & Fatigue
Joint, muscle and back pain
splenomegaly
The symptoms are like many other
febrile diseases

## Slide 72: Example for agglutination tests: Brucellosis
Image source: http://www.vet.gov.ba/

## Slide 73
Notes: Conjunctiva or broken skin contacting infected tissues Blood, urine, aborted fetuses, placentas Ingestion
  Raw milk & unpasteurized dairy products Rarely through undercooked meat

## Slide 74: Annual incidence of Brucellosis
Ariza et al, PLoS One, 2007

## Slide 75: Agglutination is used to detect antibodies against bacterial antigens (as in Wright test for brucellosis)
Agglutination of bacterial antigens with serially diluted serum samples shows the titer (concentration) of antibodies

## Slide 76: Brucellosis (Malta Fever)
Diagnosis?

## Slide 77: Diagnosis Test?
Wright test
2ME Agglutination
Coombs’ test
Rose bengal test
Complement fixation
Radioimmunoassay
ELISA

## Slide 78: Diagnosis Test?
Wright test
2ME Agglutination
Coombs’ test
Rose bengal test
Complement fixation
Radioimmunoassay
ELISA

## Slide 79: Wright test
Rapid plate agglutination test
Standard tube agglutination test (STA)

## Slide 80: Wright test 2nd week
Ab: patients serum
Ag: brucella abortus
Direct (active) agglutination

## Slide 81
Brucellosis
IgM
Acute
Chronic
IgG
Notes: Is the only antibody for the first weeks
Peaks/Drop off at about 3 months
Begins to rise in the second week
Remain elevated for > 1 year in treated patients
In relapses, IgG may be the only antibody which rises

## Slide 82: Diagnosis Test?
Wright test
2ME Agglutination
Coombs’ test
Rose bengal test
Complement fixation
Radioimmunoassay
ELISA

## Slide 83: 2-Mercaptoethanol test (2ME)
Wright test
+
destruction of disulfide bonds of IgM
IgG, IgM

## Slide 84: 2-Mercaptoethanol test (2ME)
+
Chronic!
IgG, IgM
Wright test
+
IgG, IgM

## Slide 85: 2-Mercaptoethanol test (2ME)
Acute!
IgG, IgM
Wright test
+
IgG, IgM
-

## Slide 86: Diagnosis Test?
Wright test
2ME Agglutination
Coombs’ test
Rose bengal test
Complement fixation
Radioimmunoassay
ELISA

## Slide 87: Coombs Wright
Wright
incomplete antibodies (Non agglutinating antibodies)
(IgA, IgG)
-
?

## Slide 88
Notes: rabbit anti-human globulin

## Slide 89: Diagnosis Test?
Wright test
2ME Agglutination
Coombs’ test
Rose bengal test
Complement fixation
Radioimmunoassay
ELISA

## Slide 90: Rose Bengal plate test
Rapid test, slide agglutination test
screening test
Is an agglutination test in which the brucella cells are bound to a dye
Must be confirmed by Wright test

## Slide 92: Diagnosis Test?
Wright test
2ME Agglutination
Coombs’ test
Rose bengal test
Complement fixation
Radioimmunoassay
ELISA

## Slide 93: Wright test
10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | شماره لوله
0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.9 | سرم فیزیولوژی (سی سی)
- | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.1 | سرم بیمار (سی سی)
0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | سوسپانسیون آنتی ژن
- | 5120 | 2560 | 1280 | 640 | 320 | 160 | 80 | 40 | 20 | عیار نهایی سرم
سر لوله با پارافیلم بسته شود.
24 ساعت 37 درجه
در صورت نیاز سانتریفوژ با دور 2500

## Slide 94
Titer of => 1:80 & symptoms :
brucellosis

## Slide 95: False positive results
Y. enterocolitica
V. cholera
Salmonella
Vaccines
E. coli O157

## Slide 96: False negative results
Agammaglobulinemia
First week of disease
Disease due to Br. Canis
Prozone phenomenon

## Slide 97: Salmonellosis
Clinical Symptoms: diarrhea, fever, abdominal cramps, and vomiting
Diagnostic methods: Blood Culture, Stool Culture, Serology
Serology Test: Widal

## Slide 98
IgM
IgG
O A | H A | O B | H B | O D | H D
Titer of => 1:160 & Rising Titer:
Salmonellosis

## Slide 99: Syphilis diagnosing tests
Direct Detection : Dark-Field Microscopy, Fluorescent Antibody Testing
Nontreponemal serological tests : VDRL, RPR
Treponemal serological tests: FTA-ABS test, TP-PA test, EIAs, CLIA, and multiplex flow immunoassays (MFI)
Notes: Syphilis is the most commonly acquired spirochete disease in
the United States.2,3 It is typically spread through sexual transmission.
Although the incidence of syphilis in the United States
reached an all-time low of 2.2 cases per 100,000 individuals
in 2000,4 it slowly increased to 6.3 cases/100,000 people in
2014.3 Homosexual transmission between men was responsible
for much of this increase.3,5,6 In fact, in 2000 this group
accounted for 6% of the syphilis cases in this country; in 2005,
over 60% of syphilis cases occurred in this group. By 2012,
more than 80% of cases were within this group.

## Slide 100: RPR
Sensitive, inexpensive, and simple to perform
Test Principle: Flocculation

## Slide 102: Non Infectious diagnostic serological tests

## Slide 103: Laboratory diagnostics in autoimmunity

## Slide 104: Laboratory Diagnosis of Systemic Lupus Erythematosus
CRP
ESR
C3
ANA
Anti Ds-DNA
Anti ss-DNA
Anti Histon
Anti ssa/Ro
Anti ssb/La
Anti sm
Anti DNP
Anti Jo-1
Anti SCL
Notes: ANAs are present in over 95%
of patients with active lupus and are used as a major marker for
the disease.19,25,29,36 However, ANAs are not specific for SLE
because they can also be detected in a significant percentage of
patients with other connective tissue diseases, including mixed
connective tissue disease, Sjögren’s syndrome, scleroderma

## Slide 105: Diagnostics methods for ANAs
IIF : Gold Standard, detects a wide range of antibodies, and is inexpensive, easy to perform
ELISA : automated, easy to perform, and yield objective results
sensitivities : 69% to 98%
specificities : 81% to 98%
CLIA : automated, easy to perform, and yield objective results
Microsphere Multiplex Immunoassay (MIA)

## Slide 106: Antiphospholipid Antibodies
Anti phospholipid Ab
The lupus anticoagulant ; prolonged APTT, PT
Notes: Antiphospholipid antibodies are a heterogeneous group of
antibodies that bind to phospholipids alone or phospholipids
complexed with protein. They can affect every organ in the
body, but they are especially associated with deep-vein and arterial
thrombosis and with recurrent pregnancy loss.
Ironically, patients with this
antibody have an increased risk of clotting and spontaneous
abortion.

## Slide 107
CRP

## Slide 108: CRP C-Reactive Protein
Acute Phase Protein
Inflamation
IL-1, IL-6, TNF
C3,
Serum amyloid A
CRP
Haptoglubin
Fibrinogen
Notes: Microbial infections
Acute rheumatic fever
Acute myocardial infarction
Rheumatoid Arthritis
Cancer

## Slide 109: CRP (Latex agglutination)
Reverse Passive agglutination

## Slide 110: Quality Control
Positive and Negative Control
Using non lipemic, clean, fresh sera without hemolysis
Stick to the manufacturers procedure
Also using diluted serum samples to avoid prozone phenomena is recommended.

## Slide 111: Clinical and Lab diagnosis of RA
Symptoms
Physical exam
Radiographs
labs
Notes: Recall that RF is an autoantibody, usually of the
IgM class, that reacts with the Fc portion of IgG. Approximately
70% to 90% of patients with RA test positive for RF.54,59
Thus, a negative result does not rule out the presence of RA.
Conversely, a positive test result is not specific for RA because
RF is also present in about 5% of healthy individuals and in
10% to 25% of those over the age of 65.59 In addition, RF can
be found in patients with other connective tissue diseases such
as SLE, Sjögren’s syndrome, scleroderma, and mixed connective
tissue disease, as well as in people with some chronic
infections.54,59

## Slide 112: Blood Tests
CRP
ESR
RF
Anti-CCP
Agglutination
ELISA
CLIA
Nephlometry
ELISA
Specificity : 91% to 93%.
Specificity : 75%.
Notes: RF positives: Sjögren's syndrome,hepatitis C, systemic lupus erythematosus, chronic infections
Recall that RF is an autoantibody, usually of the IgM class, that reacts with the Fc portion of IgG. Approximately 70% to 90% of patients with RA test positive for RF.54,59 Thus, a negative result does not rule out the presence of RA.
Conversely, a positive test result is not specific for RA because RF is also present in about 5% of healthy individuals and in 10% to 25% of those over the age of 65.59 In addition, RF can be found in patients with other connective tissue diseases such as SLE, Sjögren’s syndrome, scleroderma, and mixed connective tissue disease, as well as in people with some chronic infections.54,59
Manual agglutination tests using charcoal or latex particles
coated with IgG have been used for many years to detect
RF.59,61 These tests, however, only detect the IgM isotype,
found in about 75% of patients, and have been largely replaced
by ELISA, chemiluminescence immunoassay, and nephelometric
methods, which are automated, have greater precision and
sensitivity, and can also detect other RF isotypes.54,59 Testing
for IgG and IgA RFs increases test specificity. The presence of
both IgM and IgA, or of all three isotypes, rarely occurs in other
disease states, which may help in making a differential diagnosis.
In addition, testing for specific RF isotypes may have
some prognostic value. Some studies have found that IgM RF
levels decrease with clinical response to therapy and that elevation
of IgA early in the disease appears to be associated with
a poor response to TNF-α inhibitors and a worse prognosis.
These assays are performed
mainly by ELISA and use a circular synthetic form of citrullinated
peptides to increase test sensitivity, which ranges from
39% to 50%.61,62,68 About 20% to 30% of RF-negative patients
are positive for anti-CCP and the presence of anti-CCP precedes
the onset of RA by several years, making it a better
marker for early disease.

## Slide 113: RF
Immune Complex

## Slide 115: RF Latex Test
Passive(Indirect) agglutination

## Slide 117: Safety Standards and Agencies
U.S. Department of Labor, Occupational Safety and Health Administration (OSHA)
• Clinical and Laboratory Standards Institute (CLSI), a nonprofit educational organization that provides a forum for the development, promotion, and use of national and international standards
• Centers for Disease Control and Prevention (CDC), U.S. Department of Health and Human Services Public Health Service
• College of American Pathologists (CAP)
• The Joint Commission (TJC)

## Slide 118
Staff must wear laboratory coats and be additionally protected from contamination by infectious agents.
Food and drinks should not be consumed in work areas or stored in the same area as specimens. Containers, refrigerators, or freezers used for specimens should be marked as containing a biohazard.
Specimens needing centrifugation are capped and placed into a centrifuge with a sealed dome.
A gauze square is used when opening rubber-stoppered test tubes to minimize aerosol production (introduction of substances into the air).
Autodilutors or safety bulbs are used for pipetting.
Pipetting of any clinical material by mouth is strictly forbidden.
Safety Standards and Agencies

## Slide 119: Prevention of Transmission of Infectious Diseases
• According to the CDC, all human blood and other body fluids are treated as potentially infectious for HIV, HBV and ….
Educate and train all health care workers in Standard Precautions and in preventing bloodborne infections.
• Provide proper equipment and supplies (e.g., gloves).
• Monitor compliance with protective biosafety policies.

## Slide 120: quality assurance (QA) programs and quality control (QC) in Serology Lab
The introduction of routine quality assurance (QA) programs and quality control (QC) in the clinical laboratory was a major advance in improving the accuracy and reliability of testing.
This process ensures the clinician ordering the test that the testing method has been done in the best possible way to provide the most useful information in diagnosing or managing a patient.

## Slide 121: Nonanalytical Factors Related to Testing Accuracy
Qualified Personnel
Established Laboratory Policies
Laboratory Procedure Manual (SOP)
Test Requisitioning
Patient Identification, Specimen Procurement, and Labeling
Preventive Maintenance of Equipment
Appropriate Testing Methods ( regular assessment )
Inaccurate Results
Notes: patient identification data; (2) time and date of specimen
collection; (3) source of the specimen; and (4) analyses to be
performed.

## Slide 122: Tests SOP based on The Clinical and Laboratory Standards Institute (CLSI)

## Slide 123: Inaccurate Results: systematic or sporadic
Systematic errors can be eliminated by a program that monitors equipment, reagents, and other supplies.
Sporadic or isolated errors in technique can produce false-positive and false-negative results, depending on the technique used for testing

## Slide 126: Accuracy
can be improved by the following:
• Use of properly standardized procedures
• Statistically valid comparisons of new methods with established reference methods
• Use of samples of known values (controls)
• Participation in proficiency testing programs

## Slide 127
The precision of a test, its reproducibility, may be expressed as the standard deviation (SD) or derived coefficient of variation (CV).
Sensitivity and Specificity:
True positives
True negatives
False positives
False negatives
Sensitivity and Specificity

## Slide 128
Sensitivity: defined as the proportion of subjects with the specific disease positive test Result.
Specificity: defined as the proportion of subjects without the specific disease or condition who have a negative test result.

## Slide 129: Control Specimens
If the control value in a determination is out of the acceptable range :
1. Deterioration of reagents or standards
2. Faulty instrument or equipment
3. Dirty glassware
4. Lack of attention to timing or incubation temperature
5. Use of a method not suited to the needs and facilities of the laboratory
6. Use of poor technique by the technologist doing the test

## Slide 130: Validating New Procedures
The QC program includes calculation of the mean and SD and the preparation of control charts for each procedure.
If the change is to a new kit manufacturer, the new test kit must be validated for accuracy and precision. This can be done with controls, other known samples, or comparison with an old kit.
If the laboratory is receiving a new lot shipment of the same test kit, only controls need to be done.

## Slide 131: Quality Assurance in Agglutination Tests
Time of incubation with the antibody source (e.g., patient serum)
Amount and avidity of an antigen conjugated to the carrier
Conditions of the test environment (e.g., pH, protein concentration)
Adherence to strict quality control regulations (e.g., positive and negative control sera).
Proper storage of reagents and close attention to expiration dates.
Each new lot should be evaluated before use and the manufacturer’s instructions for each kit should always be followed.

## Slide 132: ……….
Agglutination tests are screening tools only and that a negative result does not rule out presence of the disease or the antigen. The quantity of antigen or antibody may be below the sensitivity of the test system.
Techniques must be standardized regarding the concentration of antigen, incubation time, temperature, diluent, and the method of reading.

## Slide 133: Quality Control in Serology Lab
Quality Control of DW
Quality Control of Centrifuge

## Slide 134: نمونه ی یک SOP : دستورالعمل روش انجام آزمایش Wright-Tube
هدف: انجام صحیح آزمایش رایت بر اساس روش لوله ای . دامنه کاربرد: این دستورالعمل جهت انجام آزمایش Wright در نمونه سرم انسانی انسان توسط روش لوله ای در بخش ایمونولوژی آزمایشگاه کاربرد دارد . صلاحیت و شایستگی کاربر: جهت حصول اطمینان از نحوه صحیح این آزمایش توسط پرسنل بخش، مطالعه کامل این دستورالعمل همراه با گذراندن دوره آزمایشی به مدت 7 روز کاری یا حداقل 5 RUN کاری تحت نظر مسوول بخش مربوطه الزامی است. اقدامات وابسته : آگاهی اساس آزمایش Wright به روش لوله ای آگاهی از محدوده رفرانس Wright در سرم و تغییر مقدار آن در بیماری های مختلف آگاهی از برنامه کنترل کیفی آزمایشگاه آشنایی با اپراتوری و تحلیل نتایج دریافت شده از دستگاه آگاهی از اصول ایمنی در آزمایشگاه نمونه لازم و موارد رد نمونه : نمونه سرم تازه. نمونه نباید همولیز ، لیپمیک و یا ایکتریک باشد. نمونه باید شفاف و فاقد هر گونه Clot و یا رشته های فیبرین باشد. حداقل حجم مورد نیاز برای سنجش Wright توسط روش اسلایدی مقدار 100 میکرولیتر می باشد. ذخیره سازی نمونه در دمای 2-8°c به مدت 7 روز ذخیره سازی نمونه در دمای -20°c جهت نگهداری طولانی مدت. نمونه های ذخیره شده در فریز بعد از دفریز شدن باید توسط ورتکس، همگن شوند. از فریز کردن نمونه هایی که قبلاً دفریز شده اند به شدت اجتناب شود . لوازم مورد نیاز : آنتی ژن مخصوص لوله ای ساخت شرکت انستیتو پاستور ایران . دستگاه روتاتور. پیپت 1ml. سمپلر 100 و 500 میکرولیتر کالیبر همراه با سر سمپلرهای نو یکبار مصرف مناسب. اپلیکاتور.چراغ مطالعه.دستکش های یکبار مصرف اساس آزمایش : اساس تكنيك مبتني بر آگلوتيناسيون مستقیم است. در صورت حضور آنتی بادی های ضد بروسلا در سرم ، این آنتی بادی ها با آنتی ژن رایت لوله ای تشکیل کمپلکس داده و آگلوتینه مشاهده می شود . روش انجام آزمایش : قبل از مصرف معرف ها و كنترل ها آنها را به دماي محيط برسانيد. به هنگام مصرف آنتی ژن رایت لوله ای، آن را به خوبي تكان دهيد تا به صورت هوموژن در آيد. تعداد 9 لوله آزمايش سرولوژي را در جا لوله اي مناسب قرار داده و در لوله اول 1ml سرم فیزیولوژی ریخته و 100 میکرولیتر از آن را بردارید و به جای آن 100 میکرولیتر از سرم را بریزید. به ساير لوله ها مقدار 0.5ml سرم فيزيولوژي بريزيد.مقدار 0.5ml از لوله اول برداشته و به لوله دوم اضافه كنيد پس از مخلوط كردن مقدار 0.5ml از آن را به لوله سوم اضافه كنيد و همين كار را تا لوله آخر ادامه دهيدو 0.5ml آخر را دور بريزيد. به تمام لوله ها مقدار 0.5ml آنتی ژن رایت لوله ای اضافه کنید. به این ترتیب تیتر ها به ترتیب 1:20-1:40 و ... می باشند. براي تهيه شاهد منفي 0.5ml آنتي ژن رقيق شده يا آماده مصرف را در يك لوله ريخته و 0.5ml سرم فیزیولوژی به آن اضافه کنید. براي تهيه شاهد مثبت 0.5ml نمونه سرم مثبت رقیق شده را به 0.5ml سرم فیزیولوژی اضافه کنید. لوله ها را به مدت 24 ساعت در انكوباتور 37 درجه سانتي گراد قرار دهید و بعد از آن زیر نور چراغ مطالعه از نظر آگلوتینه بررسی کنید. نکات ایمنی : از هرگونه خوردن و آشامیدن و کشیدن سیگار در محیط آزمایشگاه خودداری نمایید . از هرگونه تماس مستقیم با مواد بالقوه عفونت زا بدون استفاده از پوشش محافظ خودداری کنید . هرگونه محلول ریخته شده روی سطوح را توسط محلول هیپوکلریت سدیم 5% ، ضد عفونی کنید .

## Slide 135
دستورالعمل بخش سرولوژي: 1تحویل گروهی نمونه ها از نمونه گیری راس ساعت 12 همراه با لیست مربوط به بخش و چک کردن وجود یا عدم وجود هر یک از نمونه ها و مطابقت دادن با لیست ودر صورت عدم وجود نمونه مورد حتما پی گیری و به سوپر وایزر اطلاع داده شودوضمنا در فرم مربوطه(نامنطبق،اصلاحی وپیشگیرانه ثبت ونهایتا قرار دادن نمونه ها دردرب یخچال شماره 3در ردیف سرولوژی تا لحظه انجام ازمایش 2-خارج کردن محلول ها نیم ساعت قبل از شروع انجام کاراز یخچال شماره 3 تا به دمای محیط برسد 3-چک کردن تاریخ انقضای تمام محلول های مورد استفاده 4-درصورت باز کردن کیت جدیدنام کیت بایددر لیست مربوطه قید شود وتمام اصول مربوط به باز کردن که به شرح زیر است رعایت گردد: الف)وارد کردن نام وشرکت سازنده کیت ب )وارد کردن شماره سری ساخت وتاریخ انقضای کیت ج )چک خود محلول که یک دست باشد وهیچ اگلوتینه ای نداشته باشد د )چک کردن محلول به وسیله کنترل مثبت ومنفی خود کیت وکنترلهای مثبت و منفی کیت قبل ه )چک کردن محلول های کنترل مثبت و منفی کیت جدید با محلول های کیت قبلی و )چک کردن محلول های کیت جدید به وسیله ی سرم های مثبت و منفی نگهداری شده در فریزر،به عنوان کنترل سرم مثبت ومنفی ی )وارد کردن تاریخ باز کردن کیت در دفتروثبت تاریخ بر روی خود محلول 5- خارج کردن تمام سرم هااز درب یخچال وچیدن ومرتب کردن انها از روی شماره وسپس گرفتن لیست وشماره زدن ومطابقت دادن ان با لیست 6- چک کردن تمام سرم هااز نظر کیفیت(همولیز،لیپمیک،فیبرین)وکمیت ودر صورت عدم تایید ورد نمونه مورد باید حتما در فرم مربوطه(نامنطبق ،اصلاحی وپیشگیرانه)ثبت ومورد به سوپر وایزر اطلاع داده شود تا هماهنگی های لازم انجام شود. 7-شروع انجام تست ها مطابق SOPمربوط به تست های بخش سرلوژی.

## Slide 136: دستورالعمل کنترل کیفی بخش سرولوژی
1- کنترل کیفی داخلی‬ 1-1- تایید صحت عملکرد دستگاه های آنلایزرهای ایمونوسرولوژی ( رادیو ایمونواسی، لایزا، لومینومتر، فلورومتر و سایر‬ آنلایزرها ) به هنگام نصب، پس از سرویس و یا سیکل زمانی مشخص ( آزمون های دقت و صحت: شامل بلانک گیری، تکرار‬ پذیری، صحت عملکرد پروب ها / بازوها / ریل ها، پایداری دمای انکوباتور، انتقال ناخواسته نمونه، انتقال ناخواسته معرف، بررسی‬ صحت خوانش مقدار، غلظت یا فعالیت آنالیت مورد نظر )‬ نکته 1: تاییدیه صحت عملکرد دستگاه در مورد صحت خوانش مقدار، غلظت یا فعالیت آنالیت مورد نظر ممکن است توسط روش‬ مرجع، ماده مرجع، سرم کنترل، دو دستگاه مختلف و یا مقایسه بین آزمایشگاهی انجام شود.‬ نکته 2: تایید صحت عملکرد سایر تجهیزات با الزامات مربوط به هر تجهیز ( نظیر آنچه به عنوان مثال در مورد آنلایزرهای‬ ایمونوسرولوژی بیان شد ) شامل: اتو، بن ماری، سمپلرها، دیسپنسرها، پیپت ها و سایر شیشه لات حجمی، ترمومترها، سانتریفیوژر،‬ کرنومتر و غیره باید انجام شده و نتایج آن ثبت گردد.‬ 2-1- بررسی ظاهری کیت و کنترل های مصرفی از نظر پلمپ بودن، تاریخ مصرف، تغییر رنگ، شفافیت ول ها، محتویات کیت و‬ شرایط ظاهری با نمونه های قبلی‬ 3-1- بررسی نمونه های آزمایشگاهی از نظر وجود همولیز، لیپمیک، ایکتریک، فیبرین، حباب هوا و مواردی که می توانند در‬ آزمون تداخل ایجاد نمایند و ثبت آن در موارد علل رد نمونه.‬ 4-1- کنترل ماهیانه رندوم برخی از پارامترهای دستگاهی و محدوده مرجع در جوابدهی و انجام اقدام اصلاحی در صورت بروز‬ مغایرت.‬ 5-1- استفاده همزمان از حداقل دو سطح نمونه کنترل ( در صورت نبود، یک سطح و در بعضی از تست ها سه سطح ) مثالً محدوده‬ نرمال و بلا به صورت روزانه و رسم منحنی لوی جنینگ و بررسی و رعایت قوانین براساس وستگارد برای آزمون هایی که کاربری‬ بیشتری دارند و انجام و ثبت اقدام اصلاحی در مواردی که این قوانین نقض شده است.‬ 6-1- قرار دادن یک یا دو سرم کنترل و یک نمونه بیمار از ‪ Run‬قبلی در مورد تست های با پریود تکرار کمتروتست های نیمه‬ کمی و کیفی و بررسی نتیجه بدست آمده با نتیجه ومحدوده سرم کنترل و نمونه بیمار.‬ 7-1- دلتا چک روزانه تمامی نتایج غیر طبیعی( مقایسه نتایج غیر طبیعی فعلی با نتایج قبلی موجود در سوابق بیمار) این امر به منظور‬ کشف خطاهای اتفاقی در حوزه نتایج غیر طبیعی صورت می گیرد.‬ 8-1- تکرار برخی از آزمایشات که در محدوده های بحران، هشدار، بالا و پایین رنج اندازه گیری کیت قرائت شده اند و یا با بلاین‬ بیمار و سایر نتایج آزمایشگاهی وی تطابق ندارند. ( آزمایش ممکن است بر روی همان نمونه و یا نمونه جدید، با همان‬ روش/کیت/دستگاه و یا روش/کیت/دستگاهی دیگر انجام شود )‬ 9-1- استفاده از نمونه ناشناخته معلوم العیار بین کار توسط مسئول فنی، مسئول کنترل کیفی یا سوپروایزر به صورت راندوم‬ 10-1- محاسبه خطای مجاز آزمایشات اصلی و مقایسه آن با خطای مجاز بیان شده توسط مراجع ذیصلاح و در صورت لزوم انجام‬ اقدام اصلاحی‬ 11-1- تعیین و کنترل مشخصات عملکردی هر آزمایش با آنچه سازنده کیت بیان نموده است، از قبیل خطی بودن، حساسیت و‬ واکنش های تداخلی به هنگام راه اندازی آزمایش و یا تغییر در نوع کیت و یا پارامترهای دستگاه همچنین تیتراسیون با نمونه های‬ معلوم العیار در رابطه با آزمون های مرتبط‬ 21-1- نگهداری پیشگیرانه تجهیزات ایمونوسرولوژی ( ‪) PM‬‬ 31-1- رعایت استانداردهای کیفی در آماده سازی آب مقطر مصرفی، استانداردها، معرف ها، سرم کنترل ها، کلایبراتورها و به‬ ویژه محلول های ‪ Wash‬ویژه هر تست‬ 14-1- مقایسه کیت های جدید با کیت های قبلی که در آنها تغییراتی توسط سازنده بیان شده است و تصدیق و صحه گذاری آنها،‬ مثالً استفاده از کیت دیگر و یا روش دیگر برای مقایسه و کالیبراسیون در صورت وجود تفاوت قابل ملاحظه بین اختلاف میانگین‬ نتایج بیماران (‪)T-test‬‬ 51-1- استفاده از نمونه کنترل یا نمونه بیمار ‪ Positive‬در مورد تست هایی که به صورت ‪ rapid‬یا تیتراسیون لوله ای انجام می‬ گیرد و نگهداشت سوابق نتایج آن ها‬ 2- کنترل کیفی خارجی‬ 1-2- استفاده از نمونه های برنامه ارزیابی خارجی کیفیت ایمونوسرولوژی موسسات ارائه کننده نمونه های کنترل کیفی خارجی‬ ‬‬ 2-2- استفاده از نمونه سایر آزمایشگاه های مورد اطمینان و مقایسه نتایج‬ 3-2- دریافت و ارسال نمونه های مشکوک یا مجهول از آزمایشگاه های معتبر نظیر ارسال نمونه با جواب مثبت ضعیف‬ (ارزیابی مقایسه ای نتایج مشکوک در بخش هورمون و ایمونوسرولوژی)‬ 3- برنامه اجرائی تضمین کیفیت بخش ایمونوسرولوژی‬ 1-3- انجام ممیزی بر اساس چک لیست اختصاصی ایمونوسرولوژی توسط مسئول بخش / سوپروایزر/ مدیر کیفی در فواصل هر‬ سه ماه‬ 2-3- ارزیابی صلاحیت کارکنان بخش متناسب با نوع و حجم کار‬ 3-3- آموزش مستمر کارکنان بخش براساس نیازسنجی‬

## Slide 137: Still Immunology is Cool!

## Slide 138: Test Category/ Complexity point of care
1.Waived tests. Simple procedures with little chance of
negative outcomes if performed inaccurately.
2. Moderately complex tests. More complex than waived tests
but usually automated (e.g., enzyme immunoassays).
3. Highly complex tests. Usually nonautomated or complicated
tests requiring considerable judgment (e.g., serum protein
electrophoresis).
4. Provider-performed microscopy tests. Slide examinations
of freshly collected body fluids.

## Slide 139: References
HENRY’S Clinical Diagnosis AND Management BY Laboratory Methods,
23 edition, 2016
Clinical Immunology and Serology, A Laboratory Perspective, Fourth Edition, 2017
Immunology &Serology in Laboratory Medicine, Fifth edition, 2014

## Slide 140
?